## Slide 1: Bangladesh Army University of Science & Technology
Project Name: Obstacle Avoiding Robot
Course code:CSE-2200
Course title: Software Development project -II
Submitted By: Submitted to:
Muhib Al Muquit (170101018) Md. Moazzem Hossain
Rasel Rahman (170101003) Lecturer
Istiaque Ahmed (170101005) Department of CSE,BAUST
Shahinur Islam (170101043)

## Slide 2: Outline
Project idea.
Project outcome.
Working Process.
Live Application.
Future Work.
Conclusion.

## Slide 3: Project Idea
The idea is to create a obstacle avoiding robot.
We plan to attach a sensor in front of our robot and the sensor will scan every side to find ,where the maximum free space is . And the go in that direction .

## Slide 4: Project Outcome
The outcome of the project is creating a obstacle avoiding robot .
Which will go in the way it finds the maximum distance and if it finds any obstacle its stops and scans for new maximum distance.

## Slide 5: Working Process
The first step and the base of any robot is a chassis. i got mine from partex hardboard. if we prefer, we can also make your own using cardboard and DC/Servo motors. Either way, the chassis has to include a body, four motors and even a battery holder and a switch.
Now we need something that will orchestrate our motors, a micro-controller.
from the title of this instructable you probably have already understood that we are going to use Arduino.
Now simply use some screws to attach the Arduino to the chassis. we made our own chassis and find any screws, we use a small amount of glue gun. we do choose to use glue gun then search for an area under the arduino that doesn't have many pins/solder above it.

## Slide 6
In Order to make a robot that can maneuver by its own we need some sort of an input, so it can "know" or "judge" what to do. a very comfortable sensor that fits our goal (avoiding obstacles) is the Hc-sr04 ultrasonic sensor.
all we have to do next is to actually attach the servo to the body. To make life easier.

## Slide 7
Now gather some wires, and connect the sensor to the arduino according to this diagram i made.
Pay attention that our ping sensor may have a different pin layout but it should have a voltage pin, ground pin, trig pin and an echo pin.
arduino boards can't control dc motors by their own, because the currents they are generating are too low. Moreover, the currents they are generating cannot be reversed, so you can't change the direction of the motor. To solve that we will use a motor driver, which helps the arduino control dc motors. The most comfortable way of using motor drivers is through shields. Motor shields are very cheap.

## Slide 8
Take your motor shield and simply plug it into the arduino with the sensor's wires crunching inside.
Every Motor Shield has (at least) two channels, one for the motors, and one for a power source. Locate the channels and plug your chassis' motors to the motors' channel, and whatever power source you are using ( e.g. AA batteries, Lithium Battery) to the power source's channel.
After You've made your motor shield connections, From a hardware side, believe it or not, Your robot is Done. All you have to do next is to plug your arduino to your computer.

## Slide 9: Live Application

## Slide 10: Future Work
Make this Bluetooth control.
Also add camera .

## Slide 11: Conclusion
The robot works fine .In future we will try and work further and make this robot better .